Key features:

- Industrial-grade design with special vehicle port for reliable working on harsh environment

- Wide voltage support over-load ,short circuit ,reverse connect protection

- UPS power for continual work

- Basic type: support 2 SD cards & external fire box, max support 256GB

- Functional type: support 2 SD cards & external fire box, And supports 2.5' SSD, max support 2TB.

- 4G/WIFI transmit;multiple grade image quality transmitting option

- GPS/BD/GLONASS global positioning

- Powerful software platform including remote preview, playback, broadcast, talk and more

- IP communication

- PTT group talk function

- Support multiple serial port extension

## 1.Product Specifications

| Item | Description |
| --- | --- |
| OS | Linux |
| Graphics Operation Interface | System parameters can be set through external display and remote controller |
| Security Management | 2-level management for user password, administrator password, supporting encrypted transmission |
| Video and Preview | Video Input, Output | 4-channel video input, 1 channel video output; 1.0Vp-p, 75Ω |
|  | OSD | Character superposition function, information superposition of time and date, device ID and GPS, etc. |
|  | Video Compression Format | Compression coding. Applying H264 hi-performance processor. |
|  | Dual-Stream | Supported |
|  | Preview Function | Preview of 1-channle, 4-image stitching, supporting full screen triggered by event and switching of stitched images |
|  | Frame Rate | PAL: 100 frames/s, up to 25 frames/s per channel; NTSC: 120 frames/s, up to 30 frames/s per channel |
|  | Resolution | CIF, D1,and 720P for selection, supporting 4 channels of 720P at the most |
|  | Bit Rate | CIF: 384Kbps ~ 1.5 Mbps, frame rates for selection D1: 512Kbps ~ 2Mbps, frame rates for selection 720P: 2048Kbps ~ 6Mbps, frame rates for selection |
| Audio | Audio Input, Output | 4-channel input, 1-channel output |
|  | Compression Format | G.726 coding |
| Recording | Storage Medium | Basic type: support 2 SD cards&external fire box, max support 256GB Functional type: support 2 SD cards & external fire box, And supports 2.5' SSD, max support 2TB. |
|  | File Format/ System | FAT32 |
|  | Video Strategies | Recording at start up by default, supporting timed recording, recording triggered by alarm and event |
|  | Video Search | Searching by time, type, storage device and other conditions |
| Alarm | Alarm Input/ Output | 4-channel on/off signal alarm input, 2-channel on/off signal alarm output |
| Communication Ports | Support 2 channel RS232 |
| 3G/4G/WIFI | Support 3G/4G and compatible with GPRS, EDGE, .etc; built-in WiFi. |
| GPS (Optional) | Supporting GPS, optional BD/GLONASS |
| G-Sensor | Built-in G-sensor |
| System Upgrading | Supporting SD/SSD upgrading and net remote upgrading |
| Power Supply and Power Consumption | Power Supply | 1. ACC on/off 2. Delayed shutdown |
|  | Input Voltage | DC:+8V ~ +36V |
|  | Output Voltage | +12V@5*0.5A; +5V@1A |
|  | Power Consumption | <10W in normal operation |
| Operating Environment | Temperature | -25℃ ~ +60℃ |
|  | Humidity | 10% ~ 95% |
| Dimensions | 154 (W) x 39 (H) x 137(D) mm. |
| Weight | Net: 1.6KG |

### 2. Basic Working Parameters

| Item | Working Parameters | Description |
| --- | --- | --- |
| Power Supply Input | 8 ~ 36V | Input voltage at +8V~+36V, the device will be automatically turned off and enter the protection mode if the voltage is lower than 8V for a long time; if the voltage is higher than 36V for a long time, the voltage protection device will block the power supply. |
| Output Voltage | 12V | Output voltage12V (+/-0.2V), Max. current: 2A. |
| Vehicle Key Signal | ≤6V | Vehicle key off. |
|  | ≥7.5V | Vehicle key on. |
| Video Input Impedance | 75Ω | Impedance of 75Ω for each channel of video. |
| Video Output | 1Vp-p | Outputting a 1Vp-p CVBS analog signal. |
| I/O Interface | 0 ~ 2V | Low-level alarm. |
|  | Above 5V | Hi-level alarm. |
| RS232 Serial Ports | Standard Interface | Supporting 2 RS232 ports |
| SD Card Interface | Standard Interface | Compatible with commercial available brands. |

### Typical Applications

Applications: bus, school bus/staff bus, logistic trucks, coach bus, taxies, train/metro/light rail, vessels

Topological graph of main applications;

# Appearance and Accessories

### 4.1  LED Indicator

- [PWR] Power supply state indicator: LED on ─ device is powered. LED flash ─ video loss.

- [GPS] GPS signal indicator. LED on ─ GPS working. LED flash ─ GPS not work.

- [REC] REC indicator, LED flash ─ recording video. LED on ─ not recording video.

- [NET] Network indicator. LED on ─ connecting to server successfully. LED flash ─ connecting to server failed.

### 4.2  Other Definitions

- [IR] IR receiver for receiving signals from the remote controller.

- [DEBUG] DEBUG interface for research and debugging

## Definitions of External Cables

| Wire Color | Mark | Description |
| --- | --- | --- |
| White | SENSOR-IN1 | I/O alarm input 1 |
| White | SENSOR-IN2 | I/O alarm input 2 |
| White | SENSOR-IN3 | I/O alarm input 3 |
| White | SENSOR-IN4 | I/O alarm input 4 |
| White | IN-AD1 | Analog input 1 |
| White | IN-AD2 | Analog input 2 |
| Black | GND | GND |
| Red | VCC 12V | 12 v 0.5 A output |
| Pink | 5V | 5V 0.1A output |
| Blue | TXD2 | RX232 launch |
| Brown | RXD2 | RX232 receive |
| Gray | SENSOR-OUT1 | I/O alarm output 1 |
| Gray | SENSOR-OUT2 | I/O alarm output 2 |

  - Aviation interface

| Aviation interface | Mark | Description |
| --- | --- | --- |
| Black 4 core | A/V-IN1 | Audio and video channel 1 input |
| Black 4 core | A/V-IN2 | Audio and video channel 2 input |
| Black 4 core | A/V-IN3 | Audio and video channel 3 input |
| Black 4 core | A/V-IN4 | Audio and video channel 4 input |
| Black 4 core | A/V-OUT | Audio and video output |
| Black 7 core | MIC | Connecting to hand microphone |
| Black 4 core | USB | Connect the USB port and the fireproof box |
| Black 6 core | LAN | Connect the RJ45 network port |

- Infrared Remote Controller

| Key | Function | Image |
| --- | --- | --- |
|  | No use |  |
| [LOGIN] | No use |  |
| [0-9] | [0-9] keys: In the setting status, the numeric keys are used for number selection. During playback, keys 1, 2, 3 and 4 are used for switching between single window of channels 1-4, key 0 is used for switching to synchronous playback of 4 channels. |  |
|  | Returns to the preview menu or to the previous menu. |  |
| [-][+] | For adjusting the analog amount. |  |
| [DEL] | Backspace when inputting numbers. |  |
| [ENTER] | Confirms parameter selection and settings as well as operations like play. |  |
| ▲, , , | Arrow keys that move the cursor upward, downward, leftward and rightward. In the video playback screen, the right arrow key is forward fast switch key, the left arrow key is fast backward switch key. In the preview screen, the left and right direction key is the display device system status information key. |  |
|  | Snap picture |  |
|  | delete the number entered in the marquee |  |
|  | When entering network information, such as IP address, domain name, this key is consistent with ". "input role |  |
|  | Control the external access point |  |
| + | Entering the test page, check module information, and so on, for debug. |  |

# Device Setup

## Login

After turn on the device, press 【ENTER】key on the remote controller into the login menu as below, enter the correct user name and password, then press【ENTER】key into the main menu.

Default password is “999999”.

## Main Menu

After login successfully, enter the main menu as below. It includes 4 items: Playback, Preview, Settings, Tools.

## Playback

You can search all video files including normal files, alarm files by record time, file type when you enter Playback menu. Here’s the detailed description:

- Rec Type：The type of video file includes alarm file and all file. Press 【ENTER】key to select the type of video file which need to search. System default selection is all file.

## Preview

You can search all snap picture files by time when you enter preview menu. Here’s the detailed description:

- Date: Press the digit keys to setup the date，System default selection is current day.

- Start： Press the digit keys to setup the time, default time is 00:00.

OK: Select the "OK" button And press 【OK】 key to enter the following search results menu.

### Settings

Settings menu is used to set items about mdvr system config, such as encode、net etc. it is composed of 6 parts: Basic,Alarm,Net, Encode,Record,Serial.

### Basic setting

This menu is used to set mdvr time, password ,user, mirror and on/off.

- Time

This menu is used to set the time of system, including date,time, time zone and gps timing.

- Passwd

This menu is used to set user password.

- User

This menu is used to set device information ,like device number,GPS mode,license.

Mirror

This menu is used to set 1-4 channel video mirroring mode.

On/off

This menu is used to set device on/off mode.

### Alarm setting

This menu will show you how to setup the alarm parameters, include basic,input,output, alarm linkage and acceleration.

- Basic

This menu is used to set alarm input collection and alarm output linkage related parameters.

- Input

This menu is used to set I/O alarm input , support 3 channel alarm input.

- Output

This menu is used to setthe level, select the high level, then the alarm output is high

- Linkage

M32 device is 4 channel alarm setting, select corresponding alarm input setting.

- Acceleration

This menu is used to set to open and view the Gsensor value.Gsensor gravity sensor.

### Net setting

This menu will show you how to setup the system network parameters, it includes: Mode, Center, 3/4G, Net,WIFI,PTT and 808.

### Encode setting

This menu will show you how to setup the video encode parameters.

- Main stream

For selecting 720P, D1, CIF resolution types, image resolution 720P is the best, CIF is the worst

- Sub stream

For selecting parameters such as encoding mode clarity and image quality

- OSD

This menu is used to set video osd parameters.

### Record setting

This menu will show you how to setup the record strategy parameters.

- Record

Default video system PAL system, working state default automatically recording video.

- Timing record

Set the timing record，need to change to timing record mode, and modify the recording status in the record mode.

- Timing captured

Set the time for captured image to be saved automatically. If exceeding the setting time, the image

will be deleted automatically. configurable time: 1-30 days, default: 7 days.

### Serial setting

This menu will show you how to setup the serial work type and config parameters, it includes 3 sub configuration items: Serial, PTZ, POS.

- Serial

This menu is used to set serial parameters. The functions can be set as: PTZ, Transparent, temperature sensor, triple card reader, oil sensor and other peripheral serial port.

- PTZ

Set the address and protocol for the serial port to access to PTZ

## Tools

This menu includes Log management,Disk management,Operation management,Configuration management, Data export, System information.

### Log management

Log search unit lists information of all event files LOG, including event date, event time, event type.

### Disk management

Disk management is used to display disk storage info and format the SD Card(s) and external storage equipment.

Press direction keys to select “Format” button. Press 【ENTER】 key to select, system will pop up the following menu as below.

### Operation management

Operation management is used to set the equipment language and operation behavior.

### Configuration management

Restore the default settings, import and export the machine configurations.

### Data export

### System information

# Text boxes

M32 AHD MDVR

User’s Manual

4-Channel Industrial-grade AHD 720P Mobile DVR Integrating 4G, Wi-Fi, GPS functions

.