Independent design, external lens, headset, integrated MIC, 3G/4G, GPS, WIFI, Two-way talk, PTT, Portable Video recorder

Special notes: he product model photo for reference only

Content

Product Introduction	3

1	Overview	3

2	Key features	3

3	Button and indicator light identification	4

3.1	Icon 1: on/off key	4

3.2	Icon 2: alarm button	4

3.3	Icon 3: manual alarm record	4

3.4	    Icon4: photo button…………………………………...……………………… ……4  	  3.5	    Icon 5:back splint…………………………………………………………… ……4

3.6	    Icon 6: Network indicator light……………………………  ……………… ……4

3.7        Icon7:video indicator light…………………………… ……... ……………… ……4

3.8        Icon 8: power indicator light ……………………………………………………….

4	interface identification	5

5	Technical Specification	6

6	Back cover definition	7

7	connect Network configuration…………………………………………………………....8

# Product Introduction

## 1.Overview

With the industrial-grade design concept, this 4G body-worn DVR use the high-speed processor and embedded operating system, integrated with audio and video compression/global  positioning/wireless transmission/alarm and other functions as a whole.

It can be deployed in projects like outdoor remotely dispatching with different kinds of external cameras equipped and powerful CMS software system. Uses standard H.265 compression encoding, In terms of 4G transmission and local storage, it saves 40% of the transmission bandwidth and storage space compared to h.264.

## 2.Key features:

### Industrial-grade design, Ip65

### External HD camera (720p,1080p optional)

### Support blue-tooth earphone, blue-tooth hand-held mic. etc.

### H.265 compression code

### External USB, serial port interface, can extend other peripherals

### Separate DVR with camera design, Suitable for hand-held, waist-worn, shoulder-worn

- Encapsulate lithium battery power, easy for charging and carrying

## 3  Button and indicator light identification

### 3.1  Icon 1: on/off key

Long press on/off  key for 3 seconds, stop pressing after motor shook, turn into power on mode

Long press on/off  key for 4 seconds,stop pressing after motor shook, turn into power off mode

3.2  Icon 2: alarm button

Short press the alarm button, cmsv6 client will have alarm prompt. If need more linkage functions, alarm linkage can be configured in the cmsv6 client configuration, there will be sound prompts, pop-ups, interactive video, snapshot, etc.

Multiplexing function key(AP and WIFI function switching): press the on/off key&alarm button, paying attention to icon 6 light changing. If green light on, it means AP+ 4G mode. If red light on, it means WIFI+4G mode.

3.3  Icon 3: video record button

Video trigger: short press the button to start manual video record(you can set default power-on record, manual record, alarm record on the platform)

Multiplexing function key: First press the on/off key, then press video record key, when switch PTT mode , the first LED light will be red, when switch Intercom voice mode,the light will be green, at same time, the bluetooth earphone will have voice promot.

3.4  Icon4: photo button

Short press to take photos, device will shake. Playback on the CMSV6 client, search type selecting terminal Settings (image).

Multiplexing function key: press the on/off key&photo button, blue-tooth clear away matching.

3.5  Icon 5:back splint

The device can be on waist-worn, more convenient on duty.

3.6  Icon 6: Network indicator light

If green light on, it means AP+4G mode. If red light on, it means WIFI+4G mode. Find the module，light fast flash. After connect to the platform successfully, light will flash slowly.

3.7  Icon7:video indicator light

TF card in the slot, green light on. When recording video, green light flashes.When video file lost, red light on.

3.8  Icon 8: power indicator light

When charging, red light on. After full charge, green light on.If the device isn’t in charge, when power more than 50%, green light on. When power more than 25%, green light flash slowly. When power less than 25%, green light flash fast.

Notice:when  updating, Icon 6 and Icon 7 red light will flash flash by turns.

## Interface identification

Icon 1:  Connect the external camera

Icon 2:  Charge& Data output

Icon 3:  SIM card slot

Icon 4:  TF card slot

## Technical Specification

| Item | Description |
| --- | --- |
| OS | Linux |
| Industrial design | portable design,meet various application scenarios demand flexible |
| Video and Preview | Video Output, Input | Special external camera |
|  | OSD | Character superposition function, information superposition of time and date, device ID and GPS, etc. |
|  | Video Compression Format | H.265 Compression coding. Applying Hisilicon 3516C hi-performance processor. |
|  | Dual-Stream | Supported |
|  | Resolution | 1080P/720P/D1 option |
|  | Bit Rate | D1: 512kbps, 768kbps, 1024kbps, 1536kbps, 2048kbps, 5 grades adjustable 720P: 1024kbps, 2048kbps, 3072kbps, 4096kbps, 5120kbps, 5 grades adjustable 1080P: 2048kbps, 3072kbps, 4096kbps, 5120kbps, 6144kbps, 5 grades adjustable |
| Audio | Audio Input | Bluetooth device input |
|  | Audio Output | Bluetooth device input |
|  | Compression Format | G.726 coding |
| Recording | Storage Medium | Support 1pc TF card, max support 256gb, support cycle recording video. |
|  | Video Strategies | Default power-on record, support alarm record, etc |
|  | Video search | Search according to date、time or type on the CMSV6 |
|  | CAN | Don’t support |
| Positioning | Built-in GPS |
| G-sensor | Built-in |
| Network | 3G,4G,WIFI optional |
| System upgrade | Support TF card upgrading, CMSV6 client upgrading |
| Screen parameters | Size | 2.4 inch LCD |
|  | Type | TFT |
|  | Resolution | 480*234 |
| Power Supply and Power Consumption | Power supply management | manual on/off Wide voltage support over-load ,short circuit ,reverse connect protection |
|  | Voltage input | DC12 V |
|  | Power Consumption | Standard working state: 4W |
| Operating Environment | Temperature | Normal: -20℃ ~ +55℃ |
|  | Humidity | 10% to 95% |
| Dimensions | 50(W) x104(H) x27(D) mm. |
| Weight | Net: 188 g |

## 6. Bluetooth headset configuration

After turning on the device, blue-tooth will open automatically, when detects paired blue-tooth headset within 10 meters, they will be paired automatically.

### Bluetooth headset operation  introduction

#### Long press blue-tooth headset power button for 2 seconds, blue light on, it means blue-tooth  headset turns on.

#### Long press blue-tooth headset power button for 6 seconds, red and blue light flash in turns, it means blue-tooth  headset paired mode.

## 7. Connect Network configuration

7.1 Switch network mode to AP+3G/4G, (operation according to Icon 6). Use phone to search WIFI hot pot, WIFI name is DVS-88888(the number is device ID), WIFI password is 999999999. (as following picture shows)

7.2 Type 192.168.42.100 in the browser, enter into WEB configuration .( as following picture shows)

7.3 System information, you will see GPS module, 3G/4G module, WIFI module, CMS module, DISK module, I/O module, etc..

7.4  Language changing, English and Chinese optional. ( as following picture shows)

7.5  Basic setting basic information, typing device ID, Select adjusting automatically. (as following picture shows)

7.6 Network setting

7.6.1 Platform setting, connecting server’s IP and port, port ID is 6608, needn’t modify.

7.6.2 Every time enter into WIFI configuration, AP mode by default. If you  need configure WIFI client mode, please choose WIFI type. (as following picture shows)

7.6.3 Choose client mode, type WIFI SSID and password, remember to save. (as following picture shows)

7.6.4 Select 3G/4G network type

WCDMA/LTE-FDD:3G/4G

TD-SCDMA/LTE-TDD:3G/4G

EVDO: 3G

LTE-CTLTE: 4G

7.6.5 PTT parameters configuration

Please login CMSV6 client to configure(as following pictures)

7.6.5 More parameters configuration

Please login CMSV6 client to configure.

# Text boxes

M72 3G/4G Portable DVR

User Manual V1.0